## Slide 1: Ch.1.
Radioisotopes (Unstable isotopes)
  The isotopes do radioactive decay
  Mode of radioactive decay
From https://commons.wikimedia.org/wiki/Image:Radioactive_decay_modes.svg?uselang=ko

## Slide 2
  List of the radioactive ebvironmental isotopes  See Table 1-3 on p.17.
    T
      Formed by H-bomb testing (and minorly from cosmic ray bombardment on 14N)
      Daughter: 3He
      Measured in absolute amount (in TU). 1 TU=1 T per 1018H
      Detected w/ LSC or gas counter (for the case of propane preparation) (see text)

## Slide 3
    14C
      Formed by cosmic ray bombardment on 14N
      Daughter: 14N
      Measured against modern carbon (mC) whose 14C activity is 95% of that of 1950 NBS-oxalic acid standard
      Due to the fractionation, should be normalized to d13C = -25‰
      Converted into graphite and analyzed with AMS

## Slide 4
    36Cl
      Formed by cosmic ray bombardment on 36Ar
      Daughter: 36Ar
      Often analyzed with AMS

## Slide 5
Significance of environmental isotopes (in hydrogeology)?
  Trace groundwater provenance
  Estimate groundwater age
  Interpretation of groundwater quality
  Understanding geochemical evolution (reactions and reaction rates) and recharge processes
  Recognizing geochemical & biogeochemical cycles of pollutants among soil-water-atmosphere

## Slide 6
Isotopic fractionation
  A process of resulting disproportion of isotopes due to their mass difference
  Physicochemical fractionation vs. Diffusive fractionation: Compare the equations on p. 22 to 25.
  Equilibrium vs. kinetic fractionation
  See Fig. 1-5 on p.23.

## Slide 7
  The conditions of isotopic equilibria requires
    Chemical equilibria: forward and backward reaction rates are same
    Enough time for mixing between reactant and product reservoir
    Enough time for complete mixing within each reservoir (homogeneity issues)
  Temperature effect on fractionation
    For an equilibrium fractionation, usually the fractionation is reciprocally proportional to T
    For an kinetic fractionation, the fractionation is dependent upon the nature of the processes (e.g. biocatalysis vs. inorganic burning)
  See Fig. 1-8 & Table 1-4 on p. 28, Fig. 1-7. on p.29, and Fig. 1-8 on p.30.

## Slide 8
Isotope Fractionation, enrichment, and separation
  Fractionation: a
  Enrichment: e
  Separation: D
  See the equations on p.31 and Fig. 1-9 on p.32.

## Slide 9
Assignments
  Solve problems 1, 3, 5, 7, and 9 on p.33 to 34.